## Slide 1: Laser Science and Coronary Laser technique
Tom Miller
Sr. National Training Manager

## Slide 2: Laser Science
Knowing how the laser works allows you to safely and effectively support cases

## Slide 3: Lasers & the Light Spectrum
Ultraviolet vs. Infrared

## Slide 4: Mechanisms of Action
 Photochemical |  Photothermal |  Photomechanical
Breaking molecular bonds | Producing thermal energy | Creating kinetic energy
Notes: 4

## Slide 5: 1: Photochemical Mechanism Breaking molecular bonds
UV light pulse hits tissue for 135 billionths of a second (135ns); the duration of the laser pulse
50 microns penetration
Billions of molecular bonds fractured per pulse
After 135 billionths of a second, laser energy is not emitted

## Slide 6: 2: Photothermal Mechanism Producing thermal energy
Absorption vibrates the molecular bonds of the plaque
Vibration of bonds heats intracellular water
Water vaporizes, molecules break apart, & cells rupture
Expanding vapor bubble forms in 100 millionths of a second (100 ms)
    - 1000 times the duration of the actual laser energy emission

## Slide 7: 3: Photomechanical Mechanism Creating kinetic energy
Expansion and collapse of vapor bubble breaks down tissue and clears by-products away from tip
By-products of ablation are water, gas, and small particles
Entire process time per pulse is 400 millionths of a second (400 μs)
  - 4000 times the duration of the actual laser energy emission

## Slide 8: Vapor Bubble
45 Fluence
60 Fluence
  The Vapor Bubble is Energy and has an acoustic effect.
  If you get too aggressive with the fluence (bigger bubble) in a tight lesion, adverse events can occur (too much energy in a tight place).
  A good practice is to be conservative on the 1st pass and create room for the larger vapor bubble on subsequent passes

## Slide 9: The 5 S’s for Laser Atherectomy

## Slide 10: ELCA Laser Catheters
Type – Concentric vs Eccentric
Size – 2/3 or 1mm rule
      3.2mm vessel = 2.0mm catheter
      2.2mm vessel = 1.4mm catheter
      In general, if vessel anatomy or size is of concern, consider downsizing catheter
      The 0.9x80 will be the default catheter

## Slide 11: Slow Advancement
20mm lesion = 20 seconds of lasing + 10 seconds of rest = 30 seconds total
(2 trains with the 0.9x80)
3 passes would = 90 seconds
Treatment time
(10 second lasing plus 5 second time out)
Advance the catheter at < 1mm/sec for optimal results
Slow with multiple passes for best results

## Slide 12: Slow Advancement is KEY!
Lumen diameter with FAST ADVANCEMENT (greater than 1 mm per second).
2.3 TURBO in 6mm tube
FAST
Simulated lesion
Lumen diameter with SLOW ADVANCEMENT (less than 1 mm per second.)
2.3 TURBO in 6mm tube
SLOW
Simulated lesion
Slow with multiple passes for best results

## Slide 13: Key Point – Slow with Multiple Passes

## Slide 14: Maximum Settings Coronary
Coronary RX | Maximum Settings | Maximum Timings
ELCA 0.9mm | 60 / 40 | 5 sec ON 10 sec OFF
ELCA 0.9mm x-80 | 80 / 80 | 10 sec ON 5 sec OFF
ELCA 1.4, 1.7, 2.0 ELCA Eccentric 1.7E, 2.0E | 60 / 40 | 5 sec ON 10 sec OFF
TT + TE will lase until you step off the petal

## Slide 15: ELCA
Coronary laser

## Slide 16: ELCA Goals

## Slide 17: Current Status of Coronary PCI

## Slide 18: AHA/ACC Coronary Lesion Grading

## Slide 19: Today’s Coronary Population
Technologies that facilitate safe and effective delivery of definitive therapy are playing a larger and more important role

## Slide 20: ELCA

## Slide 21: ELCA Technique

## Slide 22: ELCA Technique

## Slide 23: Note on Sizing – 0.9x80 is your workhorse
Why?
It goes through a 5Fr guide
Most physicians are very resistant to go above 6Fr guide for coronary
For this reason the 1.4 is the next most popular size
It is small and powerful
It has more acceptable settings
  10 seconds of lasing followed by 5 seconds of rest
  Settings up to 80/80, all other ELCA catheters are limited to 60/40
It is extremely flexible and deliverable
From a sizing perspective, it is the safest option

## Slide 24: Notes on SIZING

## Slide 25: Laser Catheter Designs
Concentric
Eccentric
1.7mm and 2.0mm
(requires a 7 or 8 French guide)

## Slide 26: ELCA Indications

## Slide 27: ELCA Contraindications

## Slide 28: Individualization of Treatment (*excluding the 0.9x80)

## Slide 29: ELCA – What Has Changed?
Improvements in Technology
+
Improvements in Technique
=
Improvements in OUTCOMES

## Slide 30: WHY Use Laser in Challenging Lesions?1
1D016406-01

## Slide 31: WHY use Laser in Challenging lesions?1
1D016406-01

## Slide 32: Novel use of a high energy excimer laser catheter for calcified and complex coronary artery lesions
Bilodeau, L. et al. (2004). Catheterization and Cardiovascular
Interventions. 62:155-161

## Slide 33: Bilodeau
ELCA data that can be positioned in terms of effectiveness of laser on:
Calcium
CTOs
0.9 X 80 at higher settings
Lesion modification
92% success rate
Recipe for Success

## Slide 34: Purpose

## Slide 35: Bilodeau

## Slide 36: Definitions and Endpoints

## Slide 37: Methods

## Slide 38: Methods

## Slide 39: Laser Protocol/Procedure

## Slide 40: Results

## Slide 41: Results

## Slide 42: Results

## Slide 43: Results

## Slide 44: Complications
Laser Complications (total) | SLT | ILT
 | 5% | 7%
Dissection | 5% | 7%
Perforation | 0% | 0%
Spasm | 0% | 0%
No Reflow/embolization | 0% | 0%
Thrombus Formation | 0% | 0%
Acute Closure | 0% | 0%
MACE rate of 8% - compares favorable with DES MACE

## Slide 45: Conclusions

## Slide 46: ELCA Case Reviews

## Slide 47: LAD CTO VIA Radial approach

## Slide 48: LAD CTO VIA Radial approach

## Slide 51: Failed PTCA/Ostial Diagonal Lesion

## Slide 52: Failed PTCA/Ostial Diagonal Lesion

## Slide 53: ELCA Tools